## Slide 1: CLASS 3

## Slide 2: CLASS 3
Review INTRODUCTION TO ASSEMBLY LANGUAGE
ADDING AND SUBSTRACTING VALUES
REGISTERS AND OPERATIONS
TRIS AND PORT REGISTERS
LED BLINK

## Slide 3: what is a “Assembly Language”?

## Slide 4
ASSEMBLY LANGUAGE IS AN EXTREMELY LOW-LEVEL PROGRAMMING LANGUAGE THAT HAS A 1-TO-1 CORRESPONDENCE TO MACHINE CODE — THE SERIES OF BINARY INSTRUCTIONS WHICH MOVE VALUES IN AND OUT OF REGISTERS IN A CPU

## Slide 5
GENERAL OPERATIONS
MOVLW 0xFF MOVWF PORTA ADDLW b101 SUBLW 25 BCF RP1
BSF RP0

## Slide 6: ADDING AND SUBSTRACTING

## Slide 7: A
A + B
MOVLW A
A + B
w
w
ADDLW B

## Slide 8
0xF0 + 0x01
LET’S PRACTICE

## Slide 9: A - B
MOVLW B
B
A - B
w
w
SUBLW A
SUBLW subtract W from Literal
Operation: k-(W)->W

## Slide 10
0xFF - 0xAA
LET’S PRACTICE

## Slide 11: REGISTERS AND OPERATIONS

## Slide 12: STATUS
To change from Bank 0 to Bank 1 we talk to the STATUS register. We do this by setting the RP0 and RP1 bits. In most cases we’ll be moving only between Bank 0 and Bank 1, thus we can just modify the value of the bit 5 of the STATUS register.

## Slide 13: TRISD is in BANK 1
BCF BCF
STATUS, RP1 STATUS, RP0
BCF STATUS, RP1 BSF STATUS, RP0
PORTD is in BANK 0

## Slide 14: TRISD is in BANK 1
BCF STATUS, RP1
BSF STATUS, RP0
PORTD is in BANK 0
BCF BCF
STATUS, RP1 STATUS, RP0

## Slide 15: STATUS
IRP | RP1 | RP0 | TO | PD | Z | DC | C
4 3 2 1 0
6 5
7
1: BANK1
0: BANK0
0: BANK0 BANK1

## Slide 16: STATUS, 5
IRP | RP1 | RP0 | TO | PD | Z | DC | C
7 6 |  | 5 | 4 3 2 1 0 |  |  |  | 
1: BANK1
0: BANK0
0: BANK0 BANK1

## Slide 17: TRISD is in BANK 1
BSF STATUS, 5
PORTD is in BANK 0
BCF STATUS, 5

## Slide 18: BANK SELECTION

## Slide 19: BANK SELECTION

## Slide 20: BANK SELECTION

## Slide 21: W REGISTER
The W register is a general register in which you can put any value that you wish. Once you have assigned a value to W, you can add it to another value, or move.

## Slide 22: MOVLW
The MOVLW command means ‘Move Literal Value Into W’, which in English means put the value that follows directly into the W register.
MOVLW 0xAA

## Slide 23: MOVWF
This instruction means “Move The Contents Of W Into The Register Address That Follows”.
MOVWF TRISB

## Slide 24: TRIS AND PORT REGISTERS

## Slide 25: TRIS
We use the TRIS Register to program a pin to be an output or an input by simply sending a 0 or a 1 to the relevant bit in the register.
MOVLW 0xFF MOVWF TRISB

## Slide 26: TRIS
USE PORT TO WRITE
USE PORT TO READ

## Slide 27: PORT
To send one of our output pins high, we simply send a ‘1’ to the corresponding bit in our PORTx register.
MOVLW 0xFF MOVWF PORTx

## Slide 28: PORTB
PB7 PB6 PB5 PB4 PB3 PB2 PB1 PB0

## Slide 29: PORTB
PB7 PB6 PB5 PB4 PB3 PB2 PB1 PB0

## Slide 30: PORTB
PB7 PB6 PB5 PB4 PB3 PB2 PB1 PB0

## Slide 31: TRISB
PORTB
PB7 PB6 PB5 PB4 PB3 PB2 PB1 PB0

## Slide 32: TRISx
MCU
PBO
input 1
PC5
output 0

## Slide 33: PORTB.0 = 1
BSF
TRISB, 0
PORTC.5 = 0
TRISC, 5
BCF

## Slide 34: TRISx
PORTB
input
MCU
PORTC
output

## Slide 35: TRISx
0xFF -> TRISB
0x00 -> TRISC

## Slide 36
TRISx
MOVLW 0xFF MOVWF TRISB CLRF TRISC

## Slide 37: TURN LEDs ON AND OFF

## Slide 38: PORTB
PB7 PB6 PB5 PB4 PB3 PB2 PB1 PB0

## Slide 39
ORG 0x00
BSF STATUS, 5
CLRF TRISB MAIN
BCF STATUS, 5 MOVLW 0xFF MOVWF PORTB END

## Slide 40: PORTB
PB7 PB6 PB5 PB4 PB3 PB2 PB1 PB0

## Slide 41
ORG 0x00
BSF STATUS, 5
CLRF TRISB MAIN
BCF STATUS, 5 MOVLW 0xAA MOVWF PORTB END

## Slide 42
PC7 PC6 PC5 PC4 PC3 PC2 PC1 PC0
PORTC

## Slide 43
PA7 PA6 PA5 PA4 PA3 PA2 PA1 PA0
PORTA

## Slide 44
PE7 PE6 PE5 PE4 PE3 PE2 PE1 PE0
PORTE

## Slide 45
WRITE AN ASSEMBLY PROGRAM IN ORDER TO TURN ON ONLY
THE FIRST THREE LEDS OF PORTB

## Slide 46
WRITE AN ASSEMBLY PROGRAM IN ORDER TO TURN ON
THE EVEN BITS OF PORTA

## Slide 47
WRITE AN ASSEMBLY PROGRAM IN ORDER TO TURN ON
THE ODD BITS OF PORTD

## Slide 48
WRITE AN ASSEMBLY PROGRAM IN ORDER TO TURN ON ONLY
THE LAST TWO LEDS OF PORTC

## Slide 49
WRITE AN ASSEMBLY PROGRAM IN ORDER TO TURN ON
THE EVEN BITS OF PORTB AND THE ODD BITS OF PORTC

## Slide 50
THANK YOU