## Slide 1: CLASS 4

## Slide 2: CLASS 3 REVIEW

## Slide 3: PORTB
PB7 PB6 PB5 PB4 PB3 PB2 PB1 PB0

## Slide 4: TURN LEDs ON AND OFF

## Slide 5: PORTB
PB7 PB6 PB5 PB4 PB3 PB2 PB1 PB0

## Slide 6
ORG 0x00
BSF STATUS, 5
CLRF TRISB MAIN
BCF STATUS, 5 MOVLW 0xFF MOVWF PORTB END

## Slide 7: PORTB
PB7 PB6 PB5 PB4 PB3 PB2 PB1 PB0

## Slide 8
ORG 0x00
BSF STATUS, 5
CLRF TRISB MAIN
BCF STATUS, 5 MOVLW 0xAA MOVWF PORTB END

## Slide 9
PC7 PC6 PC5 PC4 PC3 PC2 PC1 PC0
PORTC

## Slide 10
PA7 PA6 PA5 PA4 PA3 PA2 PA1 PA0
PORTA

## Slide 11
PE7 PE6 PE5 PE4 PE3 PE2 PE1 PE0
PORTE

## Slide 12
WRITE AN ASSEMBLY PROGRAM IN ORDER TO TURN ON ONLY
THE FIRST THREE LEDS OF PORTB

## Slide 13
WRITE AN ASSEMBLY PROGRAM IN ORDER TO TURN ON
THE EVEN BITS OF PORTA

## Slide 14
WRITE AN ASSEMBLY PROGRAM IN ORDER TO TURN ON
THE ODD BITS OF PORTD

## Slide 15
WRITE AN ASSEMBLY PROGRAM IN ORDER TO TURN ON ONLY
THE LAST TWO LEDS OF PORTC

## Slide 16
WRITE AN ASSEMBLY PROGRAM IN ORDER TO TURN ON
THE EVEN BITS OF PORTB AND THE ODD BITS OF PORTC

## Slide 17: CLASS 4
TURN ON LEDs
7-SEGMENT DISPLAY
BASICS OF CENTRAL PROCESSING UNIT

## Slide 18: TURN LEDS ON AND OFF

## Slide 19
PA7 PA6 PA5 PA4 PA3 PA2 PA1 PA0
PORTA

## Slide 20
ORG 0x00
BSF STATUS, 5
CLRF TRISA MAIN
BCF STATUS, 5 MOVLW 0x99 MOVWF PORTA END

## Slide 21: 7-SEGMENT DISPLAY

## Slide 22
7-SEGMENT DISPLAY
COMMON CATHODE

## Slide 23: 7-SEGMENT DISPLAY

## Slide 24: 7-SEGMENT DISPLAY
Decimal | DP | g | f | e | d | c | b | a | Hex
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 3F
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 06
2 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 5B
3 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 4F
4 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 66
5 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 6D
6 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 7D
7 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 07
8 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 7F
9 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 67

## Slide 25: 7-SEGMENT DISPLAY
SHOW NUMBER “0”
IN ALL THE 7-SEG DISPLAYS

## Slide 26
7-SEGMENT DISPLAY
COMMON CATHODE

## Slide 27: 7-SEGMENT DISPLAY
Decimal | DP | g | f | e | d | c | b | a | Hex | 
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 3F | 
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 06 | 
2 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 5B | 
3 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 4F | 
4 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 66 | 
5 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 6D | 
6 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 7D | 
7 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 07 | 
8 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 7F | 
9 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 67 | 

## Slide 28
ORG 0x00
BSF STATUS, 5 CLRF TRISA CLRF TRISD MAIN
BCF STATUS, 5 MOVLW 0xFF MOVWF PORTA MOVLW 0x3F MOVWF PORTD END

## Slide 29: 7-SEGMENT DISPLAY
SHOW NUMBER “5”
IN THE FIRST TWO 7-SEG DISPLAYS

## Slide 30: 7-SEGMENT DISPLAY
SHOW CHARACTER “H”
IN THE FIRST AND LAST 7-SEG DISPLAY

## Slide 31: 7-SEGMENT DISPLAY
SHOW CHARACTER “A”
IN THE SECOND AND THIRD 7-SEG DISPLAY

## Slide 32: 7-SEGMENT DISPLAY
SHOW THE 7-SEG DISPLAY OUTPUT IF PORTD=0xC9

## Slide 33: CENTRAL PROCESSING UNIT

## Slide 34: CPU
Also known as Microprocessor, handles all instructions it receives from hardware and software running on the computer

## Slide 35: INTEL PENTIUM

## Slide 36: CENTRAL PROCESSING UNIT
The processor is placed and secured into a compatible CPU socket found on the motherboard
Processors produce heat, so they are covered with a heat sink to keep them cool and running smoothly

## Slide 37: WHAT DOES THE CPU DO?

## Slide 38: WHAT DOES THE CPU DO?
Takes input from a peripheral (keyboard, mouse, printer, etc) or computer program
Interprets what it needs
Outputs information to your monitor, or perform the requested task

## Slide 39: WHAT DOES THE CPU DO?
INPUTS
OUTPUTS

## Slide 41
HISTORY
THE FIRST MICROPROCESSOR WAS THE INTEL 4004, INTRODUCED IN 1971

## Slide 42: INTEL 4004
1971

## Slide 44: 2019

## Slide 45: Intel Core i9-9900KS Processor 18 Billion Transistors

## Slide 47: COMPONENTS OF THE CPU

## Slide 48: COMPONENTS OF THE CPU
The primary components are:
The ALU (Arithmetic Logic Unit) that performs mathematical, logical, and decision operations and
The CU (Control Unit) that directs all of the processors operations.

## Slide 49: COMPONENTS OF THE CPU

## Slide 50: MACHINE CYCLE

## Slide 51: CONTROL UNIT
The control unit has the task of decoding the instructions, interpreting them by generating the appropriate signals to be sent to the executing organs at the clock pulse rate

## Slide 52: CONTROL UNIT
The control unit's activity is generally divided into three main phases:
Fetch
Decode
Execute

## Slide 53: ARITHMETIC LOGIC UNIT
The arithmetic-logic unit is formed by a set of circuits capable of performing elementary arithmetic operations such as addition, subtraction, increment, decay, multiplication, division, data exchange between registers and control operations

## Slide 54: HOW FAST DOES A CPU TRANSFER DATA?

## Slide 55: CPU TRANSFER DATA SPEED
Like any device that utilizes electrical signals, the data travels very near the speed of light, which is approximately 300,000,000 m/s

## Slide 56: CPU TRANSFER DATA SPEED
This speed depends on the medium (type of metal in the wire) through which the signal is traveling.
Most electrical signals are traveling at about 75 to 90% the speed of light.

## Slide 57
The clock speed of a CPU is the number of instructions it can process in any given second, measured in gigahertz (GHz)
CPU CLOCK SPEED

## Slide 58: CPU CLOCK SPEED
For example, a CPU has a clock speed of 1 Hz if it can process one piece of instruction every second. Extrapolating this to a more real-world example: a CPU with a clock speed of 3.0 GHz can process 3 billion instructions each second

## Slide 59: CPU CORES
Some devices have a single-core processor while others may have a dual-core (or quad- core, etc.) processor. As might already be apparent, having two processor units working side by side means that the CPU can simultaneously manage twice the instructions every second, drastically improving performance

## Slide 60: MPU ARCHITECTURE

## Slide 61
1

## Slide 62
THANK YOU